## Slide 1
PROJECT PROPOSAL
Saliva-Based
Electrochemical Biosensor
Non-Invasive Glucose Detection in Diabetic Patients
Submitted by: Yashodeep Bhawsar
Biomedical Engineering — Shri G. S. Institute of Technology & Science, Indore

## Slide 2
The Global Diabetes Burden
Why glucose monitoring still falls short of the need
589M
adults living with
diabetes worldwide (2024)
43%
of cases remain
undiagnosed (~252M people)
$1.015T
in global health
expenditure (2024)
1 / 9 sec
a diabetes-related
death occurs
Projected Growth of Global Diabetes Prevalence
Chart: 
| 2024 | 2050 (Projected)
Adults with diabetes (millions) | 589 | 900
The Core Issue
Routine care still relies on the finger-prick blood draw — invasive, painful, and a major driver of patient non-compliance, especially among children and the elderly.
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
2

## Slide 3
Why Saliva as the Diagnostic Medium?
A non-invasive alternative grounded in established biomarker correlation
Blood (SMBG)
Current clinical gold standard
Finger-prick required, multiple times daily
Painful, invasive, low compliance
Risk of infection & psychological distress
High accuracy, but poor sustainability
Saliva
Proposed alternative medium
Abundant, painless, self-collectible
Rich in systemic biomarkers
Statistically significant correlation with blood glucose (Dar et al., 2025)
Needs ultra-sensitive detection
CGM Systems
Emerging but limited
Patient-friendly, continuous data
High cost, limits adoption
Requires subcutaneous insertion
Calibration burden remains
Bottom line: Saliva offers the best balance of patient comfort and biomarker reliability — if sensitivity and selectivity challenges can be engineered around.
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
3

## Slide 4
Key Technical Challenges
Barriers that must be engineered around for clinical-grade saliva sensing
Ultra-Low Glucose Concentration
Salivary glucose is roughly 100–1000× lower than blood glucose (0.5–2.0 mg/dL fasting), demanding highly sensitive transducers.
Variable Salivary Composition
Hydration, circadian rhythm, oral hygiene, food intake, and medication all introduce variability and reproducibility challenges.
Selectivity Against Interferents
Ascorbic acid, uric acid, and dopamine are electroactive species that can confound glucose-specific signals.
No Standardized Conversion Factor
Clinical validation across diverse diabetic populations to establish a reliable saliva-to-blood conversion factor is still lacking.
This project's approach: nanomaterial-enhanced electrode surfaces combined with enzyme-based electrochemistry to meet all four challenges simultaneously.
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
4

## Slide 5
Project Objectives
General Objective: Design, fabricate, and validate a sensitive, selective, cost-effective saliva-based electrochemical biosensor for real-time non-invasive glucose monitoring.
Specific Objectives
1
Conduct a systematic literature review of saliva-based glucose sensing technologies and enzyme immobilization strategies
2
Design a modified electrode platform using biocompatible nanomaterials (AuNPs, CNTs, graphene oxide) for enhanced sensitivity
3
Immobilize glucose oxidase (GOx) and characterize detection range, LOD, sensitivity, and selectivity
4
Test with artificial and real saliva samples against clinical glucometer readings
5
Evaluate storage stability, repeatability, and interference from common salivary components
6
Assess feasibility of miniaturizing into a portable point-of-care (POC) device
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
5

## Slide 6
Methodology — Four Sequential Phases
Each phase builds on the preceding one, ensuring systematic development and validation
01
Literature Review &
Material Selection
Review 2020–2025 publications select electrode materials (GCE / SPCE) and nanomaterial modifiers.
02
Biosensor
Fabrication
Surface preparation, nanomaterial deposition (AuNPs / rGO), and GOx immobilization via glutaraldehyde/BSA cross-linking + Nafion coating.
03
Performance
Evaluation
Chronoamperometry to assess linear range, LOD, selectivity (vs. ascorbic/uric acid), and 14-day stability under refrigeration.
04
Clinical
Validation
Saliva from diabetic & non-diabetic volunteers compared to glucometer readings via Pearson correlation and Bland-Altman analysis.
Characterization techniques used throughout: Scanning Electron Microscopy (SEM), Cyclic Voltammetry (CV), and Electrochemical Impedance Spectroscopy (EIS).
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
6

## Slide 7
Performance Evaluation Parameters
Analytical benchmarks the fabricated biosensor will be tested against
Glucose Concentration: Blood vs. Saliva
Chart: 
| Blood Glucose | Salivary Glucose
Typical concentration (mg/dL) | 100 | 1.25
Salivary glucose is ~100–1000× lower than blood glucose, requiring trace-level detection sensitivity.
Target Detection Specifications
Linear Detection Range
0.01 – 5 mM
Limit of Detection (LOD)
< 1 µM
Stability Testing Window
14 days (refrigerated)
Interference Species Tested
Ascorbic acid · Uric acid · Acetaminophen
LOD Calculation Method: The Limit of Detection is calculated as three times the standard deviation of the blank signal, divided by the slope of the calibration curve — assessed via amperometric chronoamperometry across the full salivary concentration range (0.01–5 mM).
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
7

## Slide 8
Expected Outcomes
Anticipated deliverables benchmarked against current literature
Salivary–Blood Glucose Correlation Target
Chart: 
| Dar et al. (2025) Reported (r) | This Project Target (R²)
Correlation coefficient | 0.97 | 0.9
Key Deliverables
Validated prototype: 0.01–5 mM detection range, LOD < 1 µM
Comprehensive dataset — SEM morphology, CV behavior, EIS parameters, amperometric curves
Peer-reviewed manuscript or conference presentation
Proof-of-concept for future wearable / smartphone-integrated POC platform
Beyond the prototype: by removing the need for blood sampling, this biosensor can improve patient quality of life, raise monitoring frequency and compliance, and support better long-term glycemic control.
Saliva-Based Electrochemical Biosensor for Non-Invasive Glucose Detection
8

## Slide 9
Broader Impact
Removing the blood-draw barrier from routine diabetes care
Improved Quality of Life
Eliminates repeated, painful finger-pricks from daily routines
Higher Monitoring Frequency
Pain-free testing encourages more consistent glucose tracking
Better Glycemic Control
More frequent monitoring supports fewer long-term complications
Accessible & Low-Cost
Designed for resource-limited settings across India and LMICs
90% of people with diabetes live in low- and middle-income countries — where a low-cost, non-invasive sensor has the greatest potential reach.
Thank You